Serial Numbers Affected -

Reflash and Hardware:

| 211600005M to 211600229M | 214900001M to 214900125M |
| --- | --- |
| 212700453M to 212700677M | 215100001M to 215100225M |
| 213100001M to 213100225M | 220200001M to 220200225M |
| 213500001M to 213500225M | 221000001M to 221000225M |
| 214000001M to 214000225M | 221600001M to 221600225M |
| 214800001M to 214800225M | 222600001M to 222600225M |

# Text boxes

RETROFIT

PRODUCTS AFFECTED:

PART NAME & DESCRIPTION:  EEEE         Battery Charger Plus

PART NUMBER(s): EEBC500-INT

HAZARD:

During 100 A flash reprogramming mode the thermal breaker can overheat and open allowing over charging which could produce flammable gasses.  Explosion could cause serious personal injury or death.   Overheating may also cause mounting screws to melt plastic mounts and damage the battery.

ACTIONS:

- Check if your serial number is affected.

- If affected, discontinue 100 A flash reprogramming.

- Arrange to have hardware and software updated by local Snap-on repair center.  Snap-on repair center to cover $45.00 shipping per unit and parts/labor.

Top of Form

ADVISORY

December 12, 2023

If you have questions on this retrofit or need assistance contact: 1-877-762-7664 Monday-Friday, 9:00am – 5:00pm CST.

Page 1 of 3

Page 2 of 3

If you have questions on this retrofit or need assistance contact: 1-877-762-7664 Monday-Friday, 9:00am – 5:00pm CST.

Page 2 of 3

If you have questions on this retrofit or need assistance contact: 1-877-762-7664 Monday-Friday, 9:00am – 5:00pm CST.

Page 3 of 3

If you have questions on this retrofit or need assistance contact: 1-877-762-7664 Monday-Friday, 9:00am – 5:00pm CST.

Reflash Only:

| 232500005 | 232500006 | 232500007 | 232500008 |
| --- | --- | --- | --- |
| 232500013 | 232500014 | 232500015 | 232500016 |
| 232500025 | 232500026 | 232500027 | 232500028 |
| 232500033 | 232500034 | 232500035 | 232500036 |
| 232500037 | 232500038 | 232500039 | 232500040 |
| 232500041 | 232500042 | 232500043 | 232500044 |
| 232500045 | 232500046 | 232500047 | 232500048 |
| 232500049 | 232500050 | 232500051 | 232500052 |
| 232500061 | 232500062 | 232500063 | 232500064 |
| 232500073 | 232500074 | 232500075 | 232500076 |
| 232500077 | 232500078 | 232500079 | 232500080 |
| 232500081 | 232500082 | 232500083 | 232500084 |
| 232500085 | 232500086 | 232500087 | 232500088 |
| 232500093 | 232500094 | 232500095 | 232500096 |
| 232500097 | 232500098 | 232500099 | 232500100 |
| 232500101 | 232500102 | 232500103 | 232500104 |
| 232500105 | 232500106 | 232500107 | 232500108 |
| 232500109 | 232500110 | 232500111 | 232500112 |
| 232500113 | 232500114 | 232500115 | 232500116 |
| 232500117 | 232500118 | 232500119 | 232500120 |
| 232500121 | 232500122 | 232500123 | 232500124 |
| 232500125 | 232500126 | 232500127 | 232500128 |
| 232500133 | 232500134 | 232500135 | 232500136 |
| 232500145 |  | 232500147 |  |
| 232500153 | 232500154 | 232500155 | 232500156 |
| 232500157 | 232500158 | 232500159 | 232500160 |
| 232500161 | 232500162 | 232500163 | 232500164 |
| 232500201 | 232500202 | 232500203 | 232500204 |
| 232500205 | 232500206 | 232500207 | 232500208 |
| 232500209 | 232500210 | 232500211 | 232500212 |
| 232500213 | 232500214 | 232500215 | 232500216 |
| 232500217 | 232500218 | 232500219 | 232500220 |
| 232500221 | 232500222 | 232500223 | 232500224 |